PA-28-151 Normal Checklist

Preflight

Cabin

Time Log…………………………….	Verify

ARROW Documents……………….	Check

Control Lock Bungees……………...Remove

Sun Visors…………………………..	Remove

Ignition……………………………….	OFF

Avionics –Com 1&2, Intercom.……	OFF

Master	……………………………….	ON

Fuel Gauges………………………...	Check

Beacon / Nav Lights / Pitot Heat….	ON

Lights / PH / Stall Warning Horn….	Check

Beacon / Nav Lights / Pitot Heat….	OFF

Master	……………………………….	OFF

Flaps…………………………………	Down

Right Wing

Flaps…………………………………	Check

Aileron	……………………………….	Check

Wingtip………………………………	Check

Leading Edge	……………………….	Check

Tie Down…………………………….	Disconnect

Fuel Vent…………………………….	Check

Main Tire & Brake……………….....	Check

Fuel Sumps………………………….	Drain

Fuel Quantity………………………..	Check

Fuel Filler Cap………………………	Secure

PA-28-151 Normal Checklist

Nose

Engine Oil……………………………	4-6 Quarts

Cowl Plugs…………………………..	Remove

Prop & Spinner……………………...	Check

Alternator Belt………………………	Check

Air Inlet……………………………....	Check

Landing Light……………………….	Check

Nose Strut & Tire…………………...	Check

Fuel Strainer………………………...	Drain

Left Wing

Fuel Sumps………………………….	Drain

Fuel Quantity………………………..	Check

Fuel Filler Cap………………………	Check

Main Tire & Brake…………………..	Check

Fuel Vent…………………………….	Check

Tie Down…………………………….	Disconnect

Pitot Static Vane……………………	Check

Stall Warning………………………..	Check

Leading Edge……………………….	Check

Wingtip……………………………….	Check

Aileron	………………………………..Check

Flaps………………………………….Check

Empennage

Control Surfaces……………………	Check

Tie Down…………………………….	Disconnect

Baggage Door………………………	Closed

PA-28-151 Normal Checklist

Before Starting Engine

Flaps…………………………………	UP

Preflight Inspection…………………	Complete

Passengers…………………………	Briefed

Seats & Belts	……………………….	Adjusted & Locked

Tow Bar……………………………...	Verify Location

Avionics –Com 1&2, Intercom.……	OFF

Circuit Breakers…………………….	In

Starting Engine

Fuel Selector………………………..	Lowest Tank

Mixture……………………………….	Rich

Carb Heat…………………………..	COLD

Prime…………………………………	As required

Master	……………………………….	ON

Flashing Beacon……………………	ON

Brakes	……………………………….	Hold

Electric Fuel Pump…………………	ON

Throttle………………………………	3 Pumps – 1/8” Open

Propeller Area………………………	Clear

Ignition……………………………….	Start

Throttle………………………………	1000 RPM

Oil Pressure…………………………	Check

Mixture……………………………….	Lean to “R”

Electric Fuel Pump…………………	OFF

Before Taxi

Avionics –Com 1&2, Intercom.……	ON

Transponder………………………...	ALT & 1200

ATIS/AWOS………………………...	Obtain

DG & Altimeter……………………...	Set

PA-28-151 Normal Checklist

Before Takeoff

Autopilot……………………………..	Verify OFF

Brakes	……………………………….	Hold

Flight Controls………………………	Free & Correct

Flight Instruments…………………..	6-Pack SET

Fuel Selector Valve………………...	Switch to Fullest Tank

Elevator Trim………………………..	Set

Throttle………………………………	2000 RPM

Mixture……………………………….	Lean for altitude

Magnetos……………………	Max Drop	  175 RPM

Max Difference 50 RPM

Carb Heat……………………………	Test then COLD

Engine Instruments………………...	Check

Ammeter……………………………..	10-20 Amps

Vacuum……………………………..	4.5 – 5.5 inHg

Throttle………………………………	1000 RPM

Radios	……………………………….	Set

NAV Lights…………………………..	ON (After sunset)

Throttle Friction Lock	………………	Set

Flaps…………………………………	Set

Takeoff Briefing……………………..	Complete

Line Up

Doors & Windows…………………..	Closed & Locked

Electric Fuel Pump…………………	ON

Landing Light………………………..	ON

PA-28-151 Normal Checklist

After Takeoff

Fuel Pump (At least 1000’ AGL)….	OFF

Pre-Maneuver

Safe Altitude………………………...	Verify

Landing Light………………………..	ON

Clearing Turns………………………	Complete

Fuel Pump (Ground Ref Man)…….	ON

Descent & Before Landing

Seats & Belts………………………..	Adjusted & Locked

Electric Fuel Pump…………………	ON

Fuel Selector Valve………………...	Fullest Tank

Mixture……………………………….	As required

Landing Light………………………..	ON

ATIS/AWOS…………………………	Obtain

CTAF / Tower Frequency………….	SET

Altimeter……………………………..	SET

Directional Gyro…………………….	SET

Carb Heat……………………………	As required

Autopilot……………………………..	Verify OFF

PA-28-151 Normal Checklist

After Landing

Flaps…………………………………	UP

Electric Fuel Pump…………………	OFF

Carb Heat……………………………	COLD

Landing Light………………………..	OFF

Mixture……………………………….	Lean to “R”

Shutdown

Transponder………………………...	Set to 1200

Avionics –Com 1&2, Intercom.……	OFF

Magnetos……………………………	Ground Check

Mixture……………………………….	Idle Cutoff

Ignition……………………………….	OFF

Master	……………………………….	OFF

Securing

Time Log…………………………….	Record

Sun Shades………………………....	Install

Control Lock Bungees……………...Install Seatbelts…………………………….	Set

Pilot’s Window………………………	Closed

Master	……………………………….	Verify OFF

Tie Downs…………………………...	Secured

Cowl Plugs…………………………..	Install

PA-28-151 Normal Checklist

Airspeeds (MPH IAS)

Vne…………………………………...	176

Vno…………………………………...	140

Va (Max Gross Weight)……………	124

Vfe……………………………………	125

Vs1…………………………………...	65

Vso…………………………………...	58

L/D max (Best Glide)……………….	85

Vapproach…………………………..	76

Vr……………………………………..	60

Vx(Short/Soft Field)………………...	66

Vx…………………………………….	76

Vy…………………………………….	87

Vy enroute…………………………..	100

Max demo x-wind component……..	17 Knots