PA-28-151 Emergency Checklist

Engine Failure During Takeoff Run

Throttle………………………………	Idle

Brakes	……………………………….	Apply

Mixture……………………………….	Idle cutoff

Ignition……………………………….	OFF

Master	……………………………….	OFF

Engine Failure After Takeoff

Airspeed……………………………..	85 MPH IAS

Mixture……………………………….	Idle cutoff

Fuel Selector Valve………………...	OFF

Ignition……………………………….	OFF

Flaps…………………………………	As required

Master	……………………………….	OFF

Engine Failure During Flight

Airspeed……………………………..	85 MPH IAS

Suitable Landing Site………………	Obtain

Fuel Selector Valve………………...	Fullest tank

Electric Fuel Pump…………………	ON

Mixture……………………………….	As Required

Carb Heat……………………………	ON

Ignition……………………………….	Both

Primer………………………………..	In & locked

PA-28-151 Emergency Checklist

Landing Without Engine Power

Airspeed……………………………..	85 MPH IAS

Transponder………………………...	Squawk 7700

Radio…………………………………	Mayday on 121.5 Mhz

Mixture……………………………….	Idle cutoff

Electric Fuel Pump…………………	OFF

Fuel Selector Valve………………...	OFF

Ignition Switch………………………	OFF

Flaps…………………………………	As required

Master	……………………………….	OFF

Door………………………………….	Unlatch

Seat Belts & Harness………………	Tighten

Airspeed……………………………..	76 MPH IAS

Engine Fire During Start

Starter………………………………..	Continue to crank

Mixture……………………………….	Idle Cutoff

Throttle………………………………	OPEN

Electric Fuel Pump…………………	OFF

Fuel Selector Valve………………...	OFF

Master Switch……………………….	OFF

Ignition……………………………….	OFF

Aircraft……………………………….	Evacuate

Fire…………………………………...	Extinguish

PA-28-151 Emergency Checklist

Engine Fire In Flight

Fuel Selector Valve………………...	OFF

Throttle………………………………	Closed

Mixture……………………………….	Idle Cutoff

Electric Fuel Pump…………………	OFF

Cabin Heat & Defroster……………	OFF

Land as soon as practical

Electrical /Cabin Fire In Flight

Master	……………………………….	OFF

Air Vents…………………………….	OPEN

Cabin Heat…………………………..	OFF

Fire…………………………………...	Extinguish

Land as soon as practical

Loss of Fuel Pressure

Electric fuel pump…………………..	ON

Fuel Selector………………………..	Fullest tank

PA-28-151 Emergency Checklist

Open Door

Airspeed……………………………..	100 MPH IAS or Less

Cabin Vents…………………………	Close

Storm Window………………………	Open

If upper latch is open……………….	Latch

If lower latch is open	-Open top latch

-Push door further open

and close rapidly.

-Close both latches.

Alternator Failure

Verify Failure

Electrical Load………………………	Reduce

Alternator Circuit Breakers………...	Check

Alternator Switch……………………	OFF (for 1 second)

Alternator Switch……………………	ON

If no output:

Alternator Switch……………………	OFF

Nonessential Electrical Equipment	OFF

Terminate Flight as soon as practical