PA-28-151 Normal Checklist

Preflight

Cabin

Maintenance Record……………….	Check

ARROW Documents……………….	Check

Clock…………………………………	Wind & Set

Control Lock Bungees……………...Remove

EIS & Magneto Switches…………..	OFF

Avionics –Com 1&2, Intercom.……	OFF

Master	……………………………….	ON

Time Log…………………………….	Record

Fuel Gauges………………………...	Check

All External Lights…………….…….	ON

Lights / Stall Warning Horn…….….	Check

All External Lights…………….…….	OFF

Master	……………………………….	OFF

Flaps…………………………………	Down

Fuel Sample Cup…………………..	Take with you

Right Wing

Flaps…………………………………	Check

Aileron	……………………………….	Check

Wingtip………………………………	Check

Leading Edge	……………………….	Check

Tie Down…………………………….	Disconnect

Fuel Vent…………………………….	Check

Main Tire & Brake……………….....	Check

Fuel Sumps………………………….	Drain

Fuel Quantity………………………..	Check

Fuel Filler Cap………………………	Secure

PA-28-151 Normal Checklist

Nose

Engine Oil……………………………	4-6 Quarts

Cowl Plugs…………………………..	Remove

Prop & Spinner……………………...	Check

Alternator Belt………………………	Check

Air Inlet……………………………....	Check

Nose Strut & Tire…………………...	Check

Chocks……………………………….	Remove

Fuel Strainer………………………...	Drain

Left Wing

Fuel Sumps………………………….	Drain

Fuel Quantity………………………..	Check

Fuel Filler Cap………………………	Check

Main Tire & Brake…………………..	Check

Fuel Vent…………………………….	Check

Tie Down…………………………….	Disconnect

Pitot Static Vane……………………	Check

Stall Warning………………………..	Check

Leading Edge……………………….	Check

Wingtip……………………………….	Check

Aileron	………………………………..Check

Flaps………………………………….Check

Empennage

Stabilator & Trim Tab………………	Check

Tie Down…………………………….	Disconnect

Rudder……….………………………	Check

Baggage Door………………………	Closed

PA-28-151 Normal Checklist

Starting Engine

Flaps…………………………………	UP

Passengers…………………………	Briefed

Seats & Belts	……………………….	Adjusted & Locked

Tow Bar……………………………...	Verify Location

Avionics –Com 1&2, Intercom.……	OFF

Circuit Breakers…………………….	In

Fuel Selector………………………..	Lowest Tank

Mixture……………………………….	Rich

Carb Heat…………………………..	OFF

Brakes	……………………………….	Hold

Master	……………………………….	ON

Anti-Collision Light…………….…...	ON

NAV Lights…………………………..	(After sunset) ON

Prime…………………………………	As required

Electric Fuel Pump…………………	ON

Propeller Area………………………	Clear

Magneto Switch ONLY...…………..	ON

Start Button………………………….	Hold to start

Throttle………………………………	1000 RPM

Oil Pressure…………………………	Check

Mixture……………………………….	Lean to “E”

Electric Fuel Pump…………………	OFF

EIS Switch…………………………..	ON

Before Taxi

Avionics –Com 1&2, Intercom.……	ON

Transponder………………………...	ALT & 1200

GPS Database……………………...	Current

ATIS/AWOS………………………...	Obtain

Altimeter………………………...…...	Set

Ground Control / CTAF…………….	Set & Volume

PA-28-151 Normal Checklist

Taxi Check

Attitude Indicator……………………	< 5° bank

DG & Magnetic Compass………….	Turns Freely

Turn Coordinator & Inclinometer.....	Indicates Correctly

Before Takeoff

Brakes	……………………………….	Hold

Flight Controls………………………	Free & Correct

Flight Instruments…………………..	6-Pack SET

Fuel Selector Valve………………...	Switch to Fullest Tank

Elevator Trim………………………..	Set

Mixture……………………………….	Rich

Throttle………………………………	2000 RPM

Mixture……………………………….	Lean for altitude

Magneto Switch OFF………	………	Max Drop 60 RPM

Magneto Switch ON………………	RPM Return 2000 RPM

EIS Switch OFF…………………….	Max Drop 175

EIS Switch ON………………………	RPM Return 2000 RPM

Carb Heat……………………………	Test then OFF

Engine Instruments………………...	Check

Ammeter……………………………..	10-20 Amps

Throttle………………………………	1000 RPM

Tower / Departure Control Freq…..	Set & Volume

Transponder………………………...	1200 or assigned

Navigation Equipment…………...…	Set

Throttle Friction Lock	………………	Set

Flaps…………………………………	0° or 25°

Takeoff Briefing……………………..	Complete

Doors & Windows…………………..	Closed & Locked

Electric Fuel Pump…………………	ON

Landing Light………………………..	ON

Note Time +1………………………..	Cross Country

PA-28-151 Normal Checklist

After Takeoff

Fuel Pump (At least 1000’ AGL)….	OFF

Mixture……………………………….	Leaned above 5000’

Cruise

Power………………………………..	As desired

Trim…………………………………..	Set

Mixture……………………………….	100° Rich of Peak

Pre-Maneuver

Safe Altitude………………………...	Verify

Landing Light………………………..	ON

Clearing Turns………………………	Complete

Fuel Pump (Ground Ref Man)…….	ON

Descent & Before Landing

ATIS/AWOS…………………………	Obtain Altimeter……………………………..	SET

CTAF/Tower/Ground Frequency….	Set & Volume

Navigation Equipment……………...	SET

Seats & Belts………………………..	Adjusted & Locked

NAV Lights…………………………..	(After sunset) ON

Landing Light………………………..	ON

Carb Heat……………………………	As required

Electric Fuel Pump…………………	ON

Fuel Selector Valve………………...	Fullest Tank

Mixture……………………………….	As required

PA-28-151 Normal Checklist

After Landing

Mixture……………………………….	Lean to “E”

Electric Fuel Pump…………………	OFF

Landing Light………………………..	OFF

Flaps…………………………………	UP

Carb Heat……………………………	OFF

Shutdown

Transponder………………………...	Set to 1200

Avionics –Com 1&2, Intercom.……	OFF

GPS & Transponder Units…………	OFF

Mixture……………………………….	Idle Cutoff

EIS & Magneto Switches…………..	OFF

All External Lights…………………..	OFF

Tach Time…………………………...	Note

Master	……………………………….	OFF

Securing

Time Log…………………………….	Record

Pilot’s Window………………………	Closed

Sun Shades………………………....	Install

Control Lock Bungees……………...Install Seatbelts…………………………….	Set

EIS & Magneto Switches…………..	Verify OFF

Master	……………………………….	Verify OFF

Tie Downs…………………………...	Secured

Cowl Plugs…………………………..	Install

PA-28-151 Normal Checklist

Airspeeds (MPH IAS)

Vne…………………………………...	176

Vno…………………………………...	140

Va (Max Gross Weight)……………	124

Vfe……………………………………	125

Vs1…………………………………...	65

Vso…………………………………...	58

L/D max (Best Glide)……………….	85

Vapproach…………………………..	76

Vr……………………………………..	60

Vx(Short Field)……………………...	66

Vx…………………………………….	76

Vy…………………………………….	87

Vy enroute…………………………..	100

Max demo x-wind component……..	17 Knots

PA-28-151 Normal Checklist

Power Setting Table Lycoming O-360-A4M

*Wheel Fairings Removed

Standard Temperature - KTAS

| Altitude | Temp | Percent Power |
| --- | --- | --- |
|  |  | 55% | 65% | 75% |
|  |  | RPM KTAS | RPM KTAS | RPM KTAS |
| 12000 10000 8000 6000 4000 2000 | -9°C | 2400 104 | 2600 117 | N/A |
|  | -5°C | 2350 101 | 2550 114 | N/A |
|  | -1°C | 2300 99 | 2500 111 | 2625 120 |
|  | 3°C | 2275 95 | 2450 108 | 2575 118 |
|  | 7°C | 2225 93 | 2400 105 | 2525 114 |
|  | 11°C | 2175 91 | 2350 103 | 2500 111 |

Standard temperature +20°C - KTAS

| Altitude | Temp | Percent Power |
| --- | --- | --- |
|  |  | 55% | 65% | 75% |
|  |  | RPM KTAS | RPM KTAS | RPM KTAS |
| 12000 10000 8000 6000 4000 2000 | 11°C | 2425 105 | N/A | N/A |
|  | 15°C | 2375 103 | 2550 117 | N/A |
|  | 19°C | 2325 100 | 2525 114 | 2650 122 |
|  | 23°C | 2275 98 | 2475 109 | 2600 119 |
|  | 27°C | 2250 95 | 2425 106 | 2575 116 |
|  | 31°C | 2200 93 | 2375 105 | 2500 114 |

Best Power Fuel Flow Gallons Per Hour

| 55% | 65% | 75% |
| --- | --- | --- |
| 7.8 | 9 | 10.5 |